## Slide 1
HARDWARE DATA COMPRESSION · RTL · VLSI
FIFO-Based Hardware Implementation of an LZ77 Data Compressor
The sliding window is a FIFO — a reusable FIFO library driving an LZ77 codec in C and synthesizable Verilog.
PROJECT AUTHORS
Divisht Dahiya IIT Gandhinagar
Aryan Mor NIT Kurukshetra
Verilog RTL
C model
Icarus Verilog
self-checking TBs
single-command make
Notes: Title. Central thesis: LZ77's sliding window is literally a FIFO queue, so this project builds a small library of FIFOs (sync, async/CDC, streaming) and uses them as the engine for an LZ77 codec implemented twice — a C reference model and synthesizable Verilog. Everything is verified by self-checking testbenches under Icarus Verilog via a single make.

## Slide 2
ROADMAP
Agenda
A
The Algorithm
Introduction to data compression
The LZ77 sliding-window scheme
Worked example & token grammar
B
FIFO Building Blocks
Why a FIFO? (vs. array shifting)
Synchronous & Asynchronous FIFO
Revised (arbitrary-depth) FIFOs
Comparison · Stream (valid/ready) FIFO
C
LZ77 Implementation
C software reference model
Hardware LZ77 stream compressor
RTL, testbenches & simulation
Results · Conclusion · Future scope
Notes: Three acts: (A) the LZ77 algorithm, (B) the FIFO building blocks the design is made of, and (C) tying them together into a working LZ77 compressor in software and hardware, then verifying it.

## Slide 3
THE ALGORITHM
What is LZ77?
1
Lossless
Output decompresses to the exact original bytes — nothing is approximated.
2
Sliding window
A window slides across the stream; recently seen bytes stay available as a dictionary.
3
Back-references
Repeated strings are replaced by a pointer to an earlier copy, not stored again.
EACH MATCH BECOMES ONE TOKEN
( offset , length , next_char )
how far back · how many bytes · the byte that breaks the match
The sliding window
SEARCH BUFFER (history)
LOOK-AHEAD
a
b
r
a
c
a
d
a
b
r
a
cursor
Longest match found in history
"abra" → copy 4 bytes from 7 back
Notes: LZ77 is lossless: it never discards information, it just avoids repeating it. A window slides over the stream; the left part (search buffer) is history already seen, the right part (look-ahead) is upcoming bytes. When the look-ahead repeats something in history, we emit an (offset, length, next_char) token instead of raw bytes. Here 'abra' in the look-ahead already appears 7 positions back, so it is coded as copy-4-from-7.

## Slide 4
THE ALGORITHM
Worked Example · "abracadabra"
INPUT
a
0
b
1
r
2
a
3
c
4
a
5
d
6
a
7
b
8
r
9
a
10
# | offset | length | next_char | what the token means
1 | 0 | 0 | 'a' | literal — nothing seen yet
2 | 0 | 0 | 'b' | literal
3 | 0 | 0 | 'r' | literal
4 | 3 | 1 | 'c' | copy 1 from 3 back ('a'), then 'c'
5 | 5 | 1 | 'd' | copy 1 from 5 back ('a'), then 'd'
6 | 7 | 4 | EOF | copy 4 from 7 back → "abra"
Token formation
1
Scan
Search the history buffer for the longest prefix of the look-ahead.
2
Encode
Emit (offset, length) for that match — or (0,0) if none.
3
Append
Add the next single byte that broke the match.
4
Slide
Advance the cursor by length + 1 and repeat.
11 bytes → 6 tokens
Notes: Trace of the C demo (SEARCH=LOOKAHEAD=15). First three bytes are literals (empty/no-match history). Token 4 copies one 'a' from 3 back. The payoff is the last token: 'abra' at the end already occurred at the start, so it is coded as copy-4-from-7-back — one 3-byte token replaces four bytes. Cursor always advances by length+1 (the match plus the breaking character).

## Slide 5
FIFO BUILDING BLOCKS
Why a FIFO?
The sliding window is a queue: old bytes leave the back, new bytes enter the front. A FIFO is the natural hardware for it.
Array + shifting
Every new byte shifts the whole buffer
O(n) work per byte → slower
More registers & wider muxes toggling
Wastes energy re-moving stored data
Circular FIFO buffer
Data stays put — only pointers move
O(1) enqueue and dequeue
No mass shifting → faster & leaner
Perfect fit for continuous streaming
Ring buffer
wr →
← rd
pointers move,
data does not
Notes: Motivation for the whole FIFO library. A naive array implementation shifts all stored bytes every time a new one arrives — O(n) per byte and lots of needless toggling. A circular FIFO leaves the data in place and just advances a write and read pointer: O(1) enqueue/dequeue, ideal for streaming. This is why the project treats the FIFO as the central building block.

## Slide 6
FIFO BUILDING BLOCKS
Synchronous FIFO
Single clock domain · power-of-two depth · one wrap-bit trick separates full from empty
Block diagram
mem[0 : DEPTH-1]
register array
wr_ptr
rd_ptr
din →
→ dout
flags: full empty
clk drives both pointers
sync_fifo.v
// pointers carry one extra MSB (wrap bit)
reg [ADDR_WIDTH:0] wr_ptr, rd_ptr;
wire do_write = wr_en & ~full;
wire do_read = rd_en & ~empty;
always @(posedge clk) if (do_write) begin
mem[wr_ptr[ADDR_WIDTH-1:0]] <= din;
wr_ptr <= wr_ptr + 1'b1;
end // registered read: 1-cyc latency
assign empty = (wr_ptr == rd_ptr);
assign full = (wr_ptr[ADDR_WIDTH] != rd_ptr[ADDR_WIDTH])
&& (wr_ptr[AW-1:0] == rd_ptr[AW-1:0]);
Memory register array holding DEPTH words
Pointers (ADDR_WIDTH+1) bits — extra MSB = wrap bit
Flags empty: pointers equal · full: same addr, MSB differs
Notes: Simplest FIFO: one clock. Storage is a register array; a write and a read pointer index it. The clever bit is the wrap bit — pointers are one bit wider than the address, so when the low bits match you tell full from empty by whether the extra MSB differs. The read is registered, so dout is valid the cycle after rd_en. Depth must be a power of two for this MSB trick to work.

## Slide 7
VERIFICATION
Synchronous FIFO — Testbench & Waveform
tb_sync_fifo.v
1
Write phase
assert wr_en, push bytes until full is raised
2
Read phase
assert rd_en, pop bytes until empty is raised
3
Full check
writes must stall — data never overwritten
4
Empty check
reads must stall — no stale data popped
5
Self-checking
compares popped order vs pushed → PASS
Simulation waveform (illustrative timing)
clk
wr_en
din
D0
D1
D2
rd_en
dout
D0
D1
D2
empty
full
registered read:
dout valid 1 cycle after rd_en
Notes: The self-checking testbench pushes a known sequence, then reads it back, asserting full and empty behave correctly and that writes/reads stall at the boundaries. The waveform is an illustrative timing diagram (the repo simulates under Icarus Verilog): three writes load D0-D2; because the read is registered, dout appears one clock after rd_en. empty deasserts once data is present and reasserts after the buffer drains; full never triggers here since depth >> 3.

## Slide 8
FIFO BUILDING BLOCKS
Asynchronous (Dual-Clock) FIFO
Write and read on different clocks — a clock-domain crossing. Cummings-style: Gray-coded pointers + two-flop synchronizers.
WRITE DOMAIN — wclk
READ DOMAIN — rclk
wptr_full
fifomem
(dual-port)
rptr_empty
read logic
sync_w2r
sync_r2w
2-FF
Gray
Gray code: only 1 bit flips per step → a stale sample is never garbage, just one step old.
async_fifo.v
// binary -> gray (one bit changes per +1)
assign rgraynext =
(rbinnext >> 1) ^ rbinnext;
// 2-flop synchronizer (ASYNC_REG)
always @(posedge wclk)
{wq2_rptr, wq1_rptr} <=
{wq1_rptr, rptr};
Gray pointers
avoid multi-bit glitches across domains
Two-flop sync
lets metastability settle before use
Full / Empty
compared against the synced Gray pointer
Notes: When producer and consumer run on different clocks you cannot compare pointers directly — sampling a multi-bit binary pointer mid-transition gives garbage. The fix (Cliff Cummings' design): convert pointers to Gray code so exactly one bit changes per increment, then pass them through two-flop synchronizers into the other domain. Worst case you read a pointer one step stale, which is safe. Modules: fifomem, wptr_full, rptr_empty, sync_w2r, sync_r2w.

## Slide 9
VERIFICATION
Asynchronous FIFO — Testbench & Waveform
tb_async_fifo.v
1
Two clocks
independent wclk & rclk (different periods)
2
Write burst
stream data in on the fast write clock
3
Read drain
pop on the slower read clock
4
CDC settle
allow 2-FF synchronizer latency before flags
5
Data integrity
every byte crosses intact, in order → PASS
Dual-clock waveform
CDC latency: the Gray write-pointer crosses via the 2-FF synchronizer before rempty can fall.
wclk
winc
wdata
A0
A1
A2
A3
rclk
rinc
rdata
A0
A1
rempty
Notes: Same idea, two clocks. Data is written on the faster wclk; the read side runs on a slower rclk. The read side cannot pop a byte until the Gray-coded write pointer has propagated through its two-flop synchronizer — that is the CDC latency between rempty deasserting and the write. The testbench streams a burst in and drains it out, checking every byte crosses intact and in order.

## Slide 10
FIFO BUILDING BLOCKS
Revised Synchronous FIFO
The MSB-wrap trick only works when DEPTH is a power of two. The revised design supports ANY depth.
Original
Depth locked to 2^k. Full/empty rely on natural binary overflow of the pointer's MSB — breaks for depth 12, 100, ...
Revised
Arbitrary depth. An explicit count register + modulo-DEPTH pointer rollover replaces the MSB trick.
1
Explicit count
full = (count==DEPTH), empty = (count==0) — exact, any depth
2
Modulo rollover
pointers wrap at DEPTH, not at 2^k
3
Same interface
identical ports & registered read — a drop-in upgrade
revised_sync_fifo.v
localparam ADDR_WIDTH = $clog2(DEPTH);
reg [ADDR_WIDTH:0] count; // occupancy
assign full = (count == DEPTH);
assign empty = (count == 0);
// modulo-DEPTH wrap (not 2^k overflow)
if (wr_ptr == DEPTH-1) wr_ptr <= 0;
else wr_ptr <= wr_ptr + 1;
Notes: The plain sync/async FIFOs assume power-of-two depth because they exploit natural binary overflow of the wrap bit. The revised versions relax that: they keep an explicit occupancy count and roll the pointer over at DEPTH. Full is count==DEPTH, empty is count==0 — exact for any depth. Ports and behaviour are otherwise identical, so it is a drop-in replacement.

## Slide 11
FIFO BUILDING BLOCKS
Revised Asynchronous FIFO
Arbitrary-depth CDC FIFO — the hardest case: exact flags AND safe clock-domain crossing together.
✓
Accurate full flag
Depth-aware comparison instead of the two-MSB Gray test, so non-power-of-two depths report full correctly.
⚙
Cleaner pointer logic
Binary counters bounded by DEPTH, converted to Gray only for crossing — arithmetic stays simple.
↻
Robust synchronization
Two-flop Gray synchronizers retained on both sides; metastability protection is never sacrificed for flexibility.
⚠ Same module names
The revised modules reuse the names sync_fifo / async_fifo / fifomem, so never compile an original and its revised twin into one simulation. The Makefile builds each testbench against exactly the files it needs.
Notes: The revised async FIFO combines both hard requirements: arbitrary depth AND clock-domain crossing. It keeps the two-flop Gray synchronizers (never compromising metastability safety) but uses depth-aware full detection. Practical caveat: the revised modules deliberately keep the same names as the originals, so you must not link both into one sim — the Makefile handles this by compiling each testbench against only the files it needs.

## Slide 12
FIFO BUILDING BLOCKS
FIFO Comparison
Feature | Sync FIFO | Async FIFO | Revised Sync | Revised Async
Clock domains | Single | Dual | Single | Dual
Complexity | Low | High | Medium | High
Synchronizer | No | Yes (2-FF) | No | Yes (2-FF)
Depth support | Power of 2 | Power of 2 | Arbitrary | Arbitrary
Full detection | Wrap bit | Gray + MSBs | Count reg | Depth-aware
Pointer coding | Binary | Gray | Binary | Gray
Best used for | Same-clock buffer | CDC bridge | Odd-size buffer | Odd-size CDC
Design rule: single clock → sync; crossing clocks → async (Gray + 2-FF); odd depth → the revised variants. The streaming FIFO (next) adds a valid/ready interface on top.
Notes: The core comparison slide. Sync is the cheapest for a same-clock buffer. Async adds Gray coding and two-flop synchronizers to bridge clock domains, at higher complexity. The revised variants trade the neat power-of-two trick for an explicit count so they handle any depth. Which to pick follows directly from two questions: one clock or two, and is the depth a power of two.

## Slide 13
FIFO BUILDING BLOCKS
Stream FIFO (valid / ready)
LZ77 receives a continuous byte stream, so the buffer needs flow control. This FWFT FIFO speaks an AXI-Stream-like handshake and carries an end-of-stream last bit.
Producer
Stream
FIFO
Consumer
s_valid →
← s_ready
m_valid →
← m_ready
a beat moves only when valid && ready
s_ready = ~full
accept a byte whenever there is room
m_valid = ~empty
present a byte whenever one is buffered
FWFT
first word falls through — zero read latency
last bit
end-of-stream travels with the data
stream_fifo.v
reg [DW:0] mem [0:DEPTH-1]; // {last, data}
assign s_ready = ~full;
assign m_valid = ~empty;
assign {m_last, m_data} = mem[rptr[AW-1:0]]; // FWFT
wire do_wr = s_valid & s_ready;
wire do_rd = m_valid & m_ready;
// a beat = valid && ready on either side
Why it matters for LZ77
lz77_stream_compress → stream_fifo → lz77_stream_decompress
Chaining stages with proper backpressure — no stage overruns the next. This is exactly how tb_lz77_stream.v wires the streaming path together.
Notes: The streaming FIFO wraps the same ring buffer in a valid/ready handshake. s_ready is just ~full, m_valid is ~empty, and a transfer happens only when both valid and ready are high — that gives automatic backpressure. First-word-fall-through means data is presented combinationally with zero read latency, ideal for chaining blocks. It also carries a last bit so end-of-stream propagates. This is what lets compressor → FIFO → decompressor be chained safely.

## Slide 14
VERIFICATION
Stream FIFO — Handshake Timing
The handshake rule
1
Transfer
one byte moves on every clock where valid AND ready are both high
2
Backpressure
if the consumer drops m_ready, data waits — nothing is lost
3
Stall
if the producer drops s_valid, the FIFO simply pauses
4
last
asserted with the final byte to mark end-of-stream
valid / ready handshake (illustrative timing)
clk
s_valid
s_ready
s_data
D0
D1
D2
D3
m_valid
m_ready
m_last
stall
s_ready low → producer stalls, no data lost
last marks the
final byte
Notes: Read the handshake: a byte transfers only on clocks where both valid and ready are asserted. When s_ready goes low (the shaded stall), the producer holds D2 — nothing is dropped, it just waits until ready returns. m_valid tracks data availability on the output side. The last pulse rides with the final byte so downstream logic knows the stream ended.

## Slide 15
SOFTWARE REFERENCE
LZ77 in C — the golden model
Three C programs pin down exact behaviour before any hardware is written — the RTL is verified against these.
Encoder loop
Read input
Scan search window
Find longest match
Emit (off, len, char)
Slide window
Repeat →
lz77_compressor.c — matching loop
// scan the search buffer for the longest
// matching prefix of the look-ahead
for (int i = search_start; i < cursor; i++) {
int len = 0;
while (len < LOOKAHEAD_SIZE &&
cursor+len < input_len &&
input[i+len] == input[cursor+len])
len++;
if (len > best_length) { // strictly longer
best_length = len;
best_offset = cursor - i;
}
}
cursor += best_length + 1; // slide window
lz77_compressor.c Array-based demo — dumps the token table (offset,length,char)
lz77_fifo_implementation.c Sliding window IS a circular FIFO — enqueue / dequeue / peek
lz77_robust.c Self-verifying codec: compress → decompress round-trip, incl. overlap
Notes: Software comes first as the golden reference. The matching loop is the heart of it: for each history position, count how far the look-ahead keeps matching, keep the strictly-longest match, then advance the cursor by length+1. Three programs: a token-dump demo, a version that makes the FIFO-as-window explicit, and lz77_robust.c which self-verifies via a compress/decompress round-trip. The classic RTL is byte-for-byte compatible with lz77_robust.c.

## Slide 16
HARDWARE IMPLEMENTATION
Hardware LZ77 Stream Compressor
Dataflow architecture — bytes in on a handshake, tokens out on a handshake, only a sliding window is ever held.
Input
stream
byte + valid/ready + last
Stream
FIFO
buffers & applies backpressure
Search
engine
scans history for a prefix match
Longest
match
tracks best (offset, length)
Token
generator
emits offset · length · next_char
Compressed
output
token bytes + last
Internal state held by the compressor
hist[ ] circular history window (the search buffer) look[ ] small look-ahead shift register hcount / lcount valid-byte counters
256
WINDOW
255
MAX_OFFSET
16
LOOKAHEAD
15
MAX_MATCH
Notes: The streaming compressor as a pipeline: bytes enter through a stream FIFO (backpressure), a search engine scans the history window for the longest prefix of the look-ahead, the best (offset,length) is tracked, and a token generator emits offset, length and the breaking character. Crucially only a sliding window is stored — no whole frame is buffered. State: hist[] history window, look[] look-ahead, and their counters. Default sizes shown at the bottom.

## Slide 17
HARDWARE IMPLEMENTATION
LZ77 Stream — RTL & FSM
Compressor FSM
S_FILL
fill look-ahead
from the input
S_SEARCH
scan history for
longest match
S_E0
emit offset
S_E1
emit length
S_E2
emit next_char
S_ADV
advance window
by length+1
S_DONE
last asserted
FILL → SEARCH → E0 → E1 → E2 → ADV → (loop)
lz77_stream.v — emit path
// match source: history for k<d, else the
// look-ahead itself (handles overlap len>off)
wire src = (k < d) ? hist[sidx] : look[k-d];
wire can_extend = (k < maxm) && (src==look[k]);
assign m_valid = (state==S_E0)||(state==S_E1)
||(state==S_E2);
assign m_data = (state==S_E0) ? best_off :
(state==S_E1) ? best_len :
look[best_len];
assign m_last = (state==S_E2) && final_tok;
Inputs s_valid · s_data · s_last · m_ready · clk · rst_n
Outputs s_ready · m_valid · m_data · m_last
Matching engine extends a candidate byte-by-byte; keeps best (off,len)
Overlap len > offset works — source falls through into look-ahead
Notes: The compressor is a small FSM: FILL the look-ahead, SEARCH history for the longest match, then E0/E1/E2 emit offset, length and next_char across three handshake beats, ADV slides the window by length+1, and it loops (DONE on the final token). The clever RTL line is the match source: for k<d it reads history, otherwise it reads the look-ahead itself — that is what makes overlap (length>offset, i.e. run-length) matches work, since the decoder copies one byte per cycle.

## Slide 18
VERIFICATION
LZ77 Stream — Testbench
tb_lz77_stream.v drives the full streaming path and self-checks the round-trip.
stimulus
byte stream + last
compress
lz77_stream_compress
stream_fifo
backpressure buffer
decompress
lz77_stream_decompress
checker
compare vs original
What the bench drives
1
Clock & reset
generates clk and an active-low reset pulse
2
Input stream
feeds test bytes with valid/last, honouring s_ready
3
Backpressure
toggles m_ready to exercise stalls
4
Expected output
reconstructed bytes must equal the input
Self-checking verdict
✓ ROUND-TRIP OK
Toolchain: Icarus Verilog (iverilog + vvp), gcc for the C models.
One command: make builds the 3 C models and runs all five testbenches.
Notes: tb_lz77_stream.v wires the whole streaming path — compressor, stream FIFO, decompressor — and drives it with clock/reset, a byte stream with last, and a toggling m_ready to force backpressure stalls. Being self-checking, it reconstructs the data and asserts it equals the original, printing ROUND-TRIP OK. The whole repo builds and verifies under Icarus Verilog with a single make.

## Slide 19
SIMULATION
LZ77 Stream — Compressing in Action
clk
s_valid
s_data
a
b
r
a
state
FILL
SRCH
E0
E1
E2
ADV
DONE
m_valid
m_data
off=7
len=4
'a'
m_last
① fill
② search
③ emit
④ last
① Fill
look-ahead loads bytes
② Search
history scanned for match
③ Emit
offset · length · next_char
④ Last
end-of-stream flagged
Notes: The strongest slide: the streaming compressor caught mid-operation on the abracadabra tail. The look-ahead FILLs, the FSM enters SEARCH and finds 'abra' four bytes back, then across three handshake beats (E0/E1/E2) it emits offset=7, length=4 and the next character, with m_last flagging end-of-stream. Four labelled phases map the waveform to the FSM. (Illustrative timing; the design simulates under Icarus Verilog.)

## Slide 20
THE BIG PICTURE
Overall Project Flow
Input data stream
Stream FIFO
valid / ready · last
Sliding window
hist[ ] history + look[ ] ahead
Matching engine
longest prefix match
offset
how far back
length
how many bytes
next_char
breaking byte
Software layer (C)
Golden reference model. lz77_robust.c self-verifies via compress → decompress round-trips and defines the exact token grammar the RTL must match.
Compressed output
Classic codec stream: [4-byte length] then repeated 3-byte tokens.
Overlap (len > offset) handled — decoder copies one byte per cycle.
Notes: One diagram tying it together. Data flows in through the stream FIFO, populates the sliding window (history + look-ahead), the matching engine finds the longest match, and every match becomes the three token fields offset/length/next_char that form the compressed output. On the left, the C model is the golden reference; on the right, the classic codec's on-wire format (4-byte length + 3-byte tokens), with the overlap case handled by copying one byte per cycle.

## Slide 21
OUTCOMES
Results
✓
All FIFO modules verified
sync, async, revised sync & async — self-checking benches pass
✓
Stream FIFO works
valid/ready + FWFT + last, with correct backpressure
✓
LZ77 software verified
round-trip compress/decompress incl. overlap matches
✓
Hardware LZ77 verified
classic + streaming codecs pass their testbenches
✓
Byte-exact vs C model
classic RTL matches lz77_robust.c byte-for-byte
✓
Continuous streaming
dataflow path chains stages with no frame buffering
make → builds 3 C models + runs all 5 testbenches → PASS / ROUND-TRIP OK
Notes: Everything the project set out to build is verified. All four FIFO variants pass their self-checking benches; the streaming FIFO's handshake and backpressure work; the C reference round-trips including the tricky overlap case; both RTL codecs pass; the classic codec is byte-exact against the C golden model; and the streaming path runs continuously with no whole-frame buffering. A single make reproduces all of it.

## Slide 22
IN SUMMARY
Conclusion
1
A reusable FIFO library
Synchronous, asynchronous (CDC), revised arbitrary-depth, and streaming FIFOs — each self-verified.
2
A software golden model
LZ77 in C that pins the token grammar and self-checks via round-trips.
3
Synthesizable LZ77 in Verilog
Block (memory-mapped) and streaming (handshake) codecs, byte-exact to the C reference.
4
Fully verified end-to-end
Every FIFO and codec ships with a self-checking bench; one make validates the whole design.
The sliding window is a FIFO — so a well-built FIFO library is the whole engine of an LZ77 compressor.
Notes: Wrap-up. The project delivered a reusable, self-verified FIFO library; a C golden model that fixes exact behaviour; two synthesizable LZ77 codecs that match it byte-for-byte; and complete end-to-end verification via one make. The unifying idea throughout: the LZ77 sliding window is a FIFO, so getting the FIFOs right is most of the compressor.

## Slide 23
WHAT'S NEXT
Future Scope
Performance
1
Pipeline the matching engine
overlap search & emit for higher throughput
2
Parallel matching units
compare many offsets per cycle
3
Real-time high-speed compression
sustain line-rate on fast links
Compression ratio
1
Larger search buffer
find longer / farther-back matches
2
Huffman back-end
entropy-code the token stream (→ DEFLATE-like)
3
Higher compression ratio
tune window & match limits
Silicon path
1
FPGA implementation
synthesize, place & route, measure Fmax / LUTs
2
ASIC design
push toward a hardened compression block
Notes: Future directions in three buckets. Performance: pipeline and parallelize the matching engine toward real-time line-rate compression. Ratio: a bigger search window plus a Huffman entropy back-end would push this toward a DEFLATE-style pipeline. Silicon: take the RTL through FPGA implementation (Fmax, resource use) and eventually an ASIC-hardened compression block.